## Slide 1: CEN416: Assembly Language Programming
COURSE LECTURERS
TIWALADE ODU (Engr.)
OMORUYI OSEMWEGIE (Engr.)

## Slide 2: Week 2 Topics
Instruction set and dependency on underlying processor.

## Slide 3: Instruction Set Architecture
Instruction set architecture is the structure of a computer that a machine language programmer must understand to write a correct (timing independent) program for that machine.
The instruction set architecture is also the machine description that a hardware designer must understand to design a correct implementation of the computer.
Sometimes known as The Programmer’s Model of the machine.
Instruction set architecture - ISA refers to the actual programmer visible machine interface such as instruction set, data representation, addressing, registers, memory organization and exception (i.e. interrupt) handling.

## Slide 4: Instruction Set
  The instruction set is the entire repertoire of machine operations.
  The structure of an internal instruction word and the decoding method are defined by the instruction format.
The instruction format defines the instruction word lengths, the subdivision into bit fields and interpretation method for particular fields.
Simple Instruction Format

## Slide 5: Instruction Set
The bit fields of an instruction word are used to: encode operations to be performed in the instruction,encode the decoding method for the instruction and to set some data in the instruction.
The simplest instruction format is composed of two fields: operation code (op code) field, operand address field.

## Slide 6: Instruction word cont’d
The instruction word of a computer can have fixed or variable length. In the latter case, the length of the instruction word depends on its operation code and can be determined only after decoding of this code.
Fixed and variable length instruction length

## Slide 7: Instruction word cont’d
The operation code can be composed of one or more fields. In each field we encode in a binary way mutually exclusive operations, which are to be performed in a given instruction.
In the address field we place operand addresses of the operation stated in the operation code (addresses of memory cells or registers) or the so called immediate arguments i.e. binary data immediately useful for instruction execution.
Instruction word structure

## Slide 8: Internal Instruction List
In a von Neumann computer, execution of all programs (even those written in high-level languages) consists in execution of internal instruction sequences, which are contained in binary forms of these programs.
Internal instructions represent almost all operations that a computer can perform. This does not concern operations, which are not programmable by the user of the computer. Such operations are said to be 'hardwired or wired in', as for example interrupt handling or cache functioning.

## Slide 9: Internal Instruction List
The set of all internal instructions provided in a given computer (understood as a set of operations defined by these instructions) is called computer instruction list or computer instruction set.
Based on the type of operation performed in an instruction, we distinguish the following types of internal computer instructions:
arithmetical-logical instructions,
data transfer instructions,
bit manipulation instructions,
program control instructions,
system instructions.

## Slide 10: Types of Operations and operands
In an internal instruction there is always specified an operation to be performed. Therefore types of instructions are similar to types of operations.
Depending on an instruction the following additional parameters can be also specified: operand addresses, address mode, i.e. how to compute the final operand address based on the address contained in the instruction (an address modification using data stored in the computer is possible), immediate data.
Internal instructions are composed as bit sequences placed in the instruction word fields. Such form is very inconvenient for a programmer.

## Slide 11: Types of Operations and operands
To make writing low-level programs easier, symbolic programming languages or assembler languages have been introduced.
In such languages, a program is expressed by instructions, which correspond to internal computer instructions but written down in an symbolic way as an association of the following elements: the symbol of the operation performed by the instruction (the mnemonic), the symbol of the address mode, values and symbols of addresses used by instructions (labels) and symbols and values of data (constants and variables).
Values of addresses and data can be expressed in different representations: decimal, hexadecimal, octal or binary but always together with the identifier of the representation used.

## Slide 12: Arithmetical instructions
Arithmetical-logical instructions include three groups of instructions: arithmetical, logical and shift instructions. Some examples coming mostly from Pentium processor instruction list are given below.
Arithmetical instructions
ADD Arithmetical sum of arguments - addition.
SUB Arithmetical difference of arguments - subtraction.
MUL Arithmetical product of arguments with single or double precision - multiplication.
DIV Division.
ABS Computation of the absolute value of the argument.
NEG Reversing the sign of the argument - negate sign.
INC Increment the argument by 1.
DEC Decrement the argument by 1.

## Slide 13: Logical instructions
AND Logical AND on arguments.
OR Logical OR on arguments.
EXOR Exclusive OR on arguments.
NOT Complement of the argument - negation.
Shift instructions
SHL/SHR Logical shift of the argument - shift left / shift right.
SAL/SAR Arithmetical shift of the argument - shift arithmetical left / shift arithmetical right.
ROL/ROR Rotate left / rotate right the argument.

## Slide 14: Data transfer instructions
MOV Transfer between registers or a register and memory - move.
STR Transfer between memory and a register - store.
MOVSX Transfer of byte, word, double word with the sign extension from register or memory to a register - move single/double.
LEA Load effective address from memory to a register.
PUSH Transfer data from a register to the top of the stack - push.
PUSHA Transfer data from all registers to the stack - push all.
IN, OUT Data transfer in/out from input/output devices.

## Slide 15: Bit manipulation instructions
BTS Bit test and set operation, current value of a bit is copied to the CF flag and the bit is set to 1 - bit test.
BSP Bit testing for value 1; a word or a double word is searched for the first bit equal 1 and the position number of the first bit 1 is written into a register - bit set prime.
CLR Clear a register contents.
SET Set all bits in a register to 1.

## Slide 16: Program control instructions
JMP Unconditional jump.
JE/JZ Conditional jump - jump if equal/ jump if zero.
CALL Subroutine call.
RET Return from a subroutine.
LOOPE/ LOOPZ Conditional jump which executes a loop iteration if a register is equal to a target value or zero - loop if equal, loop if zero.
INT / INTO Programmed interrupt or interrupt due to an overflow - interrupt / interrupt if overflow).
SKIP Skip execution of the next instruction.
HALT Stop execution of the program.

## Slide 17: System instructions
LMSW Load a processor state word from memory or a register to the processor state register, switch to the supervisor mode - load machine status word register.
SGDT Store the global descriptor table register contents in memory.
LGDT Load global descriptor table register from a register or memory.
LSL Load segment limit to the segment register from a register or memory.
LDS Load a value to the segment pointer register from memory - load segment.
ENTER Create a frame in the stack for parameters of a procedure in a high level language - enter frame.
ESC Jump to execution of the program by the numerical co-processor - escape.
WAIT Wait for a change of the BUSY input.