## Slide 1: CEN416: Assembly Language Programming
COURSE LECTURERS
TIWALADE ODU (Engr.)
OMORUYI OSEMWEGIE (Engr.)

## Slide 2: Week 4 Topics
Assembler directives, hand-assembling, additional 80x86/Pentium instructions.

## Slide 3: Assembler directives
The assembler is a program that is used to program a computer in its native binary machine language.
A directive is a command embedded in the source code that is recognized and acted upon by the assembler.
They can assign names to memory segments and perform many other housekeeping tasks related to the assembler. Directives are not, by default, case sensitive.
For example, .data,. DATA, and .Data are equivalent.

## Slide 4: Functions of Assembler Directives
Defining Segments- One important function of assembler directives is to define program sections, or segments. Segments are sections of a program that have different purposes. For example, one segment can be used to define variables, and is identified by the .DATA directive: .data
The .CODE directive identifies the area of a program containing executable instructions: .code
The .STACK directive identifies the area of a program holding the runtime stack, setting its size: .stack 100h

## Slide 5: Functions of Assembler Directives
Reserving space in Memory – The DWORD directive tells the assembler to reserve space in the program for a doubleword variable. val1 to val3 below are examples of such directives.
val1 DWORD 2000h
val2 Byte 08h
val3 WORD 2000h
Although all assemblers for Intel processors share the same instruction set, they usually have different sets of directives.

## Slide 6: Functions of Assembler Directives
Indirect Addressing - The size is specified by the special assembler directive BYTE PTR, WORD PTR, DWORD PTR, or QWORD PTR. These directives indicate the size of the memory data addressed by the memory pointer (PTR).
The WORD PTR directive indicates to the assembler that the instruction uses a word-sized memory pointer. If the instruction moves a byte of immediate data, BYTE PTR replaces WORD PTR in the instruction. Likewise, if the instruction uses a doubleword of immediate data, the DWORD PTR directive replaces BYTE PTR. Most instructions that refer to memory through a pointer do not need the BYTE PTR, WORD PTR, or DWORD PTR directives. These directives are necessary only when it is not clear whether the operation is a byte, word, or doubleword.

## Slide 7: Functions of Assembler Directives
Type of processor - The .686 directive tells the assembler to use the Pentium Pro instruction set in the real mode, and the .686P directive tells the assembler to use the Pentium Pro protected mode instruction set.
Most modern software is written assuming that the microprocessor is a Pentium Pro or newer, so the .686 switch is often used.
Windows 95 was the first major operating system to use a 32-bit architecture that conforms to the 80386. Windows XP requires a Pentium class machine (.586 switch) using at least a 233MHz microprocessor.

## Slide 8: Common Dirrectives

## Slide 9: Common Directives

## Slide 10: Other functions
When a ? is used in place of a numeric or ASCII value, the assembler sets aside a location and does not initialize it to any specific value. (Actually, the assembler usuallystores a zero into locations specified with a?.)
The DUP (duplicate) directive creates an array, as shown in several ways in Example 4–12. A 10 DUP (?) reserves 10 locations of memory, but stores no specific value in any of the 10 locations. If a number appears within the ( ) part of the DUP statement, the assembler initializes the reserved section of memory with the data indicated.
For example, the LIST2 BYTE 10 DUP (2) instruction reserves 10 bytes of memory for array LIST2 and initializes each location with a 02H.

## Slide 11: COMPUTER DATA FORMATS
ASCII - ASCII (American Standard Code for Information Interchange) data represent alphanumeric characters in the memory of a computer system.
The standard ASCII code is a 7-bitcode, with the eighth and most significant bit used to hold parity in some antiquated systems.
If ASCII data are used with a printer, the most significant bits are a 0 for alphanumeric printing and 1 for graphics printing.
In the personal computer, an extended ASCII character set is selected by placing a 1 in the leftmost bit.
The extended ASCII characters store some foreign letters and punctuation, Greek

## Slide 12: ASCII CharSet

## Slide 13: Extended ASCII CharSet

## Slide 14: References
The Intel Microprocessor, Architecture, Programming and Interfacing, 6th Ed., by Barr B Brey.
http://deeprajbhujel.blogspot.com/2015/12
/functional-block-diagram-of-8086.html
Irvine, K. R., & Das, L. B. (2011). Assembly language for x86 processors. Prentice Hall.