## Slide 1: CEN416: Assembly Language Programming
COURSE LECTURERS
TIWALADE ODU (Engr.)
OMORUYI OSEMWEGIE (Engr.)

## Slide 2: Week 5 Topics
Modular Programming – Linker, Public and EXTRN Directives, Library Files, Macros

## Slide 3: Linker
Programs in assembly language usually require more than one person to code. This module discusses a number of tools and programs used to facilitate modular programming.
A linker is a program that is provided in assembly language to link modules into one.
Whilst an Assembler program converts a symbolic source module (file) into a hexadecimal object file(.hex).
The linker program reads the object files that are created by the assembler program and links them together into a single execution file. In our scenario, the linker program is contained in the VS 2015/17/19/22

## Slide 4: Example

## Slide 5: PUBLIC AND EXTRN
The PUBLIC and EXTRN directives are very important to modular programming because they allow communications between modules.
PUBLIC is used to declare that labels of code, data, or entire segments are available to other program modules.
EXTRN (external) declares that labels are external to a module.
Without these statements, modules could not be linked together to create a program by using modular programming techniques. They might link, but one module would not be able to communicate to another.

## Slide 6: PUBLIC AND EXTRN (continued)
The PUBLIC directive is placed in the opcode field of an assembly language statement to define a label as public, so that the label can be used by other modules. The label declared as public can be a jump address, a data address, or an entire segment.
Example: When segments are made public, they are combined with other public segments that contain data with the same segment name.

## Slide 7: PUBLIC AND EXTRN (continued)
The EXTRN statement appears in both data and code segments to define labels as external to the segment.
If data are defined as external, their sizes must be defined as BYTE, WORD, or DWORD. If a jump or call address is external, it must be defined as NEAR or FAR.

## Slide 8: Library files
Library files are collections of procedures that are used by many different programs. These procedures are assembled and compiled into a library file by the LIB program that accompanies the MASM assembler program.
Libraries allow common procedures to be collected into one place so they can be used by many different applications.
Example: the irvine32.lib file contains a collection of procedures used in our scenario.

## Slide 9: Library Files
A library file is created with the LIB command, which executes the LIB.EXE program that is supplied with Visual Studio. A library file is a collection of assembled .OBJ files that contains procedures or tasks written in assembly language or any other language.

## Slide 10: Macros
A macro is a group of instructions that perform one task, just as a procedure performs one task. The difference is that a procedure is accessed via a CALL instruction, whereas a macro, and all the instructions defined in the macro, is inserted in the program at the point of usage.
Creating a macro is very similar to creating a new opcode, which is actually a sequence of instructions, in this case, that can be used in the program. You type the name of the macro and any parameters associated with it, and the assembler then inserts them into the program.
Macro sequences execute faster than procedures because there is no CALL or RET instruction to execute.

## Slide 11: Macros (continued)
The MACRO and ENDM directives delineate a macro sequence. The first statement of a macro is the MACRO instruction, which contains the name of the macro and any parameters associated with it.
An example is MOVE MACRO A,B, which defines the macro name as MOVE.
This new pseudo opcode uses two parameters: A and B. The last statement of a macro is the ENDM instruction, which is placed on a line by itself.
Local Variables in a Macro. Sometimes, macros contain local variables. A local variable is one that appears in the macro, but is not available outside the macro. To define a local variable, we use the LOCAL directive.

## Slide 12: References
The Intel Microprocessor, Architecture, Programming and Interfacing, 8th Ed., by Barr B Brey.
Irvine, K. R., & Das, L. B. (2011). Assembly language for x86 processors. Prentice Hall.