## Slide 1: CEN416: Assembly Language Programming
COURSE LECTURERS
TIWALADE ODU (Engr.)
OMORUYI OSEMWEGIE (Engr.)

## Slide 2: Week 2 Topics
Instruction set and dependency on underlying processor.

## Slide 3: Instruction Set Architecture
Instruction set architecture is the structure of a computer that a machine language programmer must understand to write a correct (timing independent) program for that machine.
The instruction set architecture is also the machine description that a hardware designer must understand to design a correct implementation of the computer.
Sometimes known as The Programmer’s Model of the machine.
Instruction set architecture - ISA refers to the actual programmer visible machine interface such as instruction set, data representation, addressing, registers, memory organization and exception (i.e. interrupt) handling.

## Slide 4: Instruction Set
  The instruction set is the entire repertoire of machine operations.
  The structure of an internal instruction word and the decoding method are defined by the instruction format.
The instruction format defines the instruction word lengths, the subdivision into bit fields and interpretation method for particular fields.
Simple Instruction Format

## Slide 5: Instruction Set
The bit fields of an instruction word are used to: encode operations to be performed in the instruction, encode the decoding method for the instruction and to set some data in the instruction.
The simplest instruction format is composed of two fields: operation code (op code) field, operand address field.

## Slide 6: Instruction word cont’d
The instruction word of a computer can have fixed or variable length. In the latter case, the length of the instruction word depends on its operation code and can be determined only after decoding of this code.
Fixed and variable length instruction length

## Slide 7: Instruction word cont’d
The operation code (OPCODE) can be composed of one or more fields. In each field we encode in a binary way mutually exclusive operations, which are to be performed in a given instruction.
In the address field, we place operand addresses of the operation stated in the operation code (addresses of memory cells or registers) or the so called immediate arguments i.e. binary data immediately useful for instruction execution.
Instruction word structure

## Slide 8: Types of Operations and operands
In an internal instruction there is always specified an operation to be performed. Therefore types of instructions are similar to types of operations.
Depending on an instruction the following additional parameters can be also specified: operand addresses, address mode, i.e. how to compute the final operand address based on the address contained in the instruction (an address modification using data stored in the computer is possible) and immediate data.
Internal instructions are composed as bit sequences placed in the instruction word fields. Such form is very inconvenient for a programmer.

## Slide 9: Types of Operations and operands
To make writing low-level programs easier, symbolic programming languages or assembler languages have been introduced.
In such languages, a program is expressed by instructions, which correspond to internal computer instructions but written down in an symbolic way as an association of the following elements: the symbol of the operation performed by the instruction (the mnemonic), the symbol of the address mode, values and symbols of addresses used by instructions (labels) and symbols and values of data (constants and variables).
Values of addresses and data can be expressed in different representations: decimal, hexadecimal, octal or binary but always together with the identifier of the representation used.

## Slide 10: Conclusion
Thank you.